## Slide 1
Lightweight CNN Accelerator
for Real-Time Image Processing on FPGA
Xilinx Zynq-7000 SoC (xc7z020clg484-1) • Hardware/Software Co-Design
VEMANA VENKATA PUJITHRAM — 230907016
B SATVIK PRABHU — 230907178
SRI RAM THOTTEMPUDI — 230907038
Manipal Institute of Technology • JAN – MAY 2026
SoC PROJECT

## Slide 2
Motivation & Problem Statement
Why hardware acceleration?
⚠ The CPU Bottleneck
CNNs require millions of MAC operations per frame
ARM Cortex-A9 processes pixels sequentially → high latency
Real-time edge AI (drones, ADAS, cameras) demands <50 ms/frame
CPU-only solution exceeds power budget for embedded devices
✔ Hardware Acceleration
Move convolution + activation to FPGA fabric (PL)
Process 9 pixels in parallel using DSP48E1 slices
Streaming line-buffer architecture — zero stall pipeline
INT8 fixed-point: 4× lower memory bandwidth vs FP32
Target: ≥2× speedup vs. software-only • Platform: Xilinx Zynq-7000 SoC • Arithmetic: INT8 Fixed-Point

## Slide 3
System Architecture
Hardware/Software Co-Design on Zynq SoC
PS – Processing System
ARM Cortex-A9 @ 667 MHz
Image capture & preprocessing
DMA configuration & control
AXI DMA transfer (MM2S/S2MM)
Cache flush / invalidate
ASCII output post-processing
UART printf communication
AXI4-Stream
DMA
→
←
PL – Programmable Logic (FPGA)
CNN Accelerator IP @ 50–100 MHz
Line Buffer + Window Gen
↓
3×3 MAC Array (9 parallel muls)
↓
ReLU Activation (INT8 saturate)
↓
2×2 Max Pooling
FSM Controller
Zynq-7000 integrates ARM PS + FPGA PL on a single chip — data moves via high-speed AXI interconnect

## Slide 4
RTL Module Hierarchy
SystemVerilog implementation — all modules and their roles
config.sv
Global params: IMG_WIDTH=32, PIXEL_WIDTH=8, ACCUM_WIDTH=32
line_buffer.sv
2-row pixel cache — avoids DRAM re-reads (streaming architecture)
window_generator.sv
3-deep shift registers → 3×3 window; valid_out after 2×W+2 pixels
mac_array_3x3.sv
9 parallel INT8 multipliers + adder tree → 32-bit accumulator
relu_activation.sv
MSB check: clamp negative→0, saturate positive→127, output INT8
max_pool_2x2.sv
Comparator tree: max of 2×2 patch; registered synchronous output
cnn_controller.sv
3-state FSM: IDLE → BUFFER_FILL → CONV_STREAM; drives en_mac/relu/pool
cnn_accelerator_top.sv
Top-level: wires all sub-modules; hardcoded Sobel {1,0,−1,2,0,−2,1,0,−1}
+ tb_cnn.sv: 100 MHz testbench, 5×5 image, XSim sim (495 ns) | + cnn_axi_wrapper.v: AXI4-Stream shell, TLAST@899px → see Slide 8

## Slide 5
Memory Management
Streaming Architecture — Line Buffer & Window Generator
line_buffer.sv
Stores 2 rows of pixels (32 pixels each) in flip-flop arrays
On each valid_in clock: shifts pixel_in → line1, old line1 → line2
Column pointer (col) wraps at IMG_WIDTH=32
Outputs line1_out and line2_out every cycle — no stalls
Pixel Stream → Row 0 (current)
Row 1 (line1 — 1 row ago)
Row 2 (line2 — 2 rows ago)
…
…
…
← active 3-col window
window_generator.sv
Three 3-deep shift registers (shift0/shift1/shift2) — one per row
Each clock: new pixel enters shift[0]; older pixels shift right
After 2×IMG_WIDTH + 2 pixels, outputs a valid 3×3 window every cycle
Avoids all DRAM latency — pure on-chip streaming
3×3 Output Window → mac_array
p[0]
p[1]
p[2]
p[3]
p[4]
p[5]
p[6]
p[7]
p[8]
↓ (9 pixels every clock once pipeline full)

## Slide 6
Core Computation Datapath
MAC Array → ReLU Activation → 2×2 Max Pooling
mac_array_3x3.sv
9 Parallel Multipliers + Adder Tree
9 signed INT8×INT8 multiplications in parallel (combinational)
Products summed in synchronous 32-bit accumulator (ACCUM_WIDTH)
Prevents overflow during summation
Hardcoded Sobel edge kernel: {1,0,−1, 2,0,−2, 1,0,−1}
Outputs: mac_out[31:0], valid_out
mac = Σ(pixel[i] × weight[i]) for i = 0..8
→
relu_activation.sv
Non-linear Activation + INT8 Quantization
Checks MSB (bit 31) of 32-bit MAC output
Negative → output 0 (ReLU: y = max(0, x))
Positive > 127 → saturate to 8'd127 (max signed INT8)
Positive ≤ 127 → truncate mac_in[7:0]
Outputs: relu_out[7:0], valid_out
out = 0 if mac<0 | min(mac, 127) if mac≥0
→
max_pool_2x2.sv
Down-sampling by 2×2 Max Pooling
Accepts 4 INT8 pixels from a 2×2 spatial region
Two-level combinational comparator tree
max_1 = max(pool_in[0], pool_in[1])
max_2 = max(pool_in[2], pool_in[3])
pool_out = max(max_1, max_2) — registered
32×32 input → 30×30 conv → 15×15 pooled
All stages registered on posedge clk — fully pipelined. ReLU skips max_pool in current top-level (pixel_out direct from ReLU)

## Slide 7
Control Path — Finite State Machine
cnn_controller.sv: IDLE → BUFFER_FILL → CONV_STREAM
S0
IDLE
Wait for start
signal from PS
S1
BUFFER_FILL
Fill line buffers;
wait for window_valid
S2
CONV_STREAM
Pipeline active:
en_mac = en_relu = en_pool = 1
start = 1
→
window_valid
→
← !window_valid
Control Output Logic (Combinational)
State | en_mac | en_relu | en_pool
IDLE | 0 | 0 | 0
BUFFER_FILL | 0 | 0 | 0
CONV_STREAM | 1 | 1 | 1

## Slide 8
AXI DMA Integration & Block Design
cnn_axi_wrapper.v bridges the custom CNN IP to the Zynq AXI fabric
ARM
Cortex-A9
AXI DMA IP
(Xilinx)
CNN AXI
Wrapper
CNN
Accelerator
Top
DDR
RAM
AXI4
GP0
AXI4-
Stream
SV
wires
AXI4
HP0
AXI DMA — Transfer Flow
1. Start S2MM (receive) channel — RxBuffer[900] ready
2. Start MM2S (transmit) channel — push TxBuffer[1024]
3. Poll XAXIDMA_DEVICE_TO_DMA and DMA_TO_DEVICE busy flags
4. D-cache flush before TX, invalidate before RX read
cnn_axi_wrapper.v — Key Details
s_axis_tready hardwired HIGH — always accepts pixels
m_axis_tvalid = valid_out from CNN accelerator top
TLAST asserted at 899th output pixel (900 total)
Pixel counter resets after each full frame
Block Design IP Cores:
Processing System 7 (PS7)
AXI DMA 0
CNN AXI Wrapper 0
AXI Smart Connect 0
AXI Mem Interconnect
Proc Sys Reset (50 MHz)
XLConcat (IRQs)

## Slide 9
Software — ARM Cortex-A9 (main_app.c)
Bare-metal C application running on the Processing System
1
Initialize AXI DMA
XAxiDma_LookupConfig + CfgInitialize; disable all IRQs (polling mode)
2
Load Image to TxBuffer
Copy test_image[1024] into TxBuffer[1024] byte-by-byte
3
Clear RxBuffer
Zero-fill RxBuffer[900] — prevents reading stale data
4
D-Cache Flush (TX & RX)
Xil_DCacheFlushRange — ensures DMA reads updated physical RAM
5
Start S2MM then MM2S
Receive channel starts first; then transmit pushes 1024 bytes into FPGA
6
Poll Until Complete
XAxiDma_Busy() loop on both channels; waits for HW to finish
7
Invalidate Cache (RX)
Xil_DCacheInvalidateRange — forces CPU to fetch fresh data from DRAM
8
Print ASCII 30×30 Grid
pixel>60 → ## | pixel>20 → ++ | else → spaces (UART terminal)
32×32 input (1024 B) → 30×30 output (900 B) | Input: image_data.h | Output: UART ASCII art edge map

## Slide 10
Simulation & Verification
Vivado XSim Behavioral Simulation — tb_cnn.sv testbench
Testbench Setup (tb_cnn.sv)
Clock: 100 MHz (10 ns period)
Synchronous reset at startup
start signal asserted on clock 5
Test image: 5×5 hardcoded array
Bright object (0x20=32) on dark background (0x0A=10)
Pixels streamed serially into pixel_in port
Simulation completes at 495 ns
valid_out monitored to capture pixel_out stream
Waveform Observations
clk / reset:
Properly initialize system at t=0; reset de-asserts on cycle 3
pixel_in bus:
Correct hex values (0x0a=10, 0x20=32) streamed sequentially
window_valid:
Rises after 2×5+2=12 pixels — exactly when 3×3 window is full
FSM transition:
IDLE → BUFFER_FILL on start; → CONV_STREAM on window_valid
pixel_out / valid_out:
Output appears after pipeline latency; correct ReLU clamping observed
No X/Z states:
No unknown or high-impedance in CONV_STREAM — proves stable pipeline
Tool: Vivado 2025.2 XSim • Behavioral Simulation • sim_1 / tb_cnn • Run time: 1000 ns

## Slide 11
Fixed-Point Arithmetic & Design Parameters
INT8 quantization strategy and key configuration values
config.sv Parameters
Parameter | Value | Purpose
PIXEL_WIDTH | 8 bits | INT8 pixel / activation
WEIGHT_WIDTH | 8 bits | INT8 kernel weights
ACCUM_WIDTH | 32 bits | Overflow-safe accumulator
IMG_WIDTH | 32 | Input image columns
IMG_HEIGHT | 32 | Input image rows
Conv output | 30×30 | No padding, stride=1
TX bytes | 1024 | 32×32 grayscale input
RX bytes | 900 | 30×30 conv output
Why INT8 Fixed-Point?
4× Memory Bandwidth Reduction
INT8 requires 1 byte vs FP32's 4 bytes — critical for BRAM efficiency
DSP48E1 Optimization
Zynq DSP slices natively handle 18×18 signed integer multiply in one clock cycle
<1% Accuracy Loss
Established by Tiny-YOLO research — negligible for edge detection tasks
32-bit Accumulator
Product of two INT8 = 16-bit; summing 9 products needs 32-bit to prevent overflow
Hardcoded Convolution Kernel (Sobel-style Edge Detection) — cnn_accelerator_top.sv
1
0
-1
2
0
-2
1
0
-1
Detects vertical edges — strong response at horizontal intensity transitions in the 32×32 test image

## Slide 12
Conclusions & Future Work
✔ What We Achieved
Fully pipelined CNN accelerator in SystemVerilog (zero-stall streaming)
3-state FSM controller with clean state transitions
9-parallel MAC array with 32-bit accumulator (no overflow)
INT8 ReLU with saturation clamping to 127
AXI4-Stream interface (cnn_axi_wrapper.v) for DMA integration
Complete PS/PL co-design on Zynq-7000 platform
Functional simulation verified in Vivado XSim (495 ns)
Bare-metal C software with proper cache management
→ Future Work
Multi-channel CNN with 16/32 feature maps per layer
3-layer deep network (Conv → Pool → Conv → Pool → FC)
On-chip weight storage using BRAM (ping-pong buffers)
Live camera input via MIPI CSI-2 or USB UVC driver
Interrupt-driven DMA (replace polling mode)
Benchmark: measure actual FPS vs. ARM software baseline
Synthesis & place-route — measure LUT / DSP / BRAM usage
Export to deployment: Petalinux + V4L2 camera pipeline
Thank You